## Slide 1
Source: glassdoor.nl
Source: Google Maps
Source: bbc.com
Source: ed.nl
Source: mustsharenews.com
Source: plusonline.nl
Notes: Imagine it's your first week working at Albert Heijn --> Friday afternoon comes. --> things start to turn sideways. --> products left at the checkout --> on your way there you notice some fallen and misplaced products, --> lady asks you to get her an item from the top of a shelf. A lot of things happening …

## Slide 2
Source: supermarketnews.com
Notes: And of course stress and overwhelm build up.

## Slide 3
Ahold Delhaize Case: relocating products left at checkout
Group 10: - Rubén Martín Rodríguez (5507391) - Max Polak (4570677) - Pim de Ruijter (4580699) - Frankie Yuezhe Zhang (5390664) - Gioele Buriani (5629888)
Notes: We are group 10 and we are going to present a first step towards putting a solution to this problem.

## Slide 4
PROBLEM STATEMENT
"Ahold Delhaize (problem owner)​ needs a way to free their employees from time-consuming undesirable tasks (problem)​ during periods of maximum customer flow (context) in order to increase employees' performance​ and customer service (goal)"​
Notes: Just to make it clear, our client, Ahold Delhaize, needs to find a way to free their employees for these unpleasant tasks during periods of high customer flow.

## Slide 5: OUR SOLUTION
Make TIAGo return products left at the cashier to their original shelf​​
Notes: enable TIAGo to relocate products at the checkout --> simple task, but which requires most of the components

## Slide 6: STRUCTURE
GUI
Navigation
Error handling
Perception
Planning
Motion control
Notes: We will show how we achieved this by inspecting the different components and functionalities of our system, which can be seen on screen right now.

## Slide 7: GUI
Qt interface implemented in C++
Communication with system through dynamic reconfigure node
server
/params
order_req
Level
scan
charge
GUI
Other nodes
Notes: First of all, we need our robot to communicate with employees,
developed a GUI using Qt, intuitive buttons , indicator and panel for informing
integrates with the system by acting as a node, communicates reconfigurable node.

## Slide 8: GUI
Notes: displaying the "working" status and message back to the charging station.
Once it stops, the status changes to "free"
upon a click, it starts operation, "working" status in blue.

## Slide 9: NAVIGATION
Autonomous navigation:
Using gmapping for map building (SLAM)
Using amcl for self-localization (MCL)
Local obstacle avoidance
Perform sequential actions when pressing buttons.
Error handling

## Slide 10: NAVIGATION
Charging station
Checkout
Shelves

## Slide 11: ERROR HANDLING
?
No products?
Obstruction?

## Slide 12: ERROR HANDLING
text-to-speech!

## Slide 13: PERCEPTION
ArUco Tags
  Works well on close range
  Fewer false positives
Parameter server
  Send highest priority item

## Slide 14: PERCEPTION
For proper human-robot interaction
Problems at close range
Problems when rotated

## Slide 15: PLANNING – General PDDL
Construct the knowledge base only based on prior knowledge of the environment
Unable to deal with unseen environment or online request

## Slide 16: PLANNING – PDDL + update_goals
To address this issue, the update_goals node is used
To receive detected information after navigation, and integrate with the knowledge base

## Slide 17: MOTION CONTROL
Basic actions:
Gripper control
Look to point
Move base
Complex actions:
Pick
Place

## Slide 18: MOTION CONTROL

## Slide 19
TO SUM UP
GUI
Navigation
Error handling
Perception
Planning
Motion control

## Slide 20: EXTRA! FUTURE WORK
OctoMap of the shelves in RViz.
Scanning shelves possibilities:
Relocate misplaced products
Place back products fallen on the floor
Detecting the shelf emptiness for restocking notifications

## Slide 21: Are you ready to hire TIAGo?

## Slide 22: Thank you for your attention!
Group 10: Rubén Martín Rodríguez (5507391) Max Polak (4570677) Pim de Ruijter (4580699) Frankie Yuezhe Zhang (5390664) Gioele Buriani (5629888)

## Slide 23: ERROR HANDLING (EXTRA)

## Slide 24: Full Video In Simulation

## Slide 25: Full Video In Real World